## Slide 1: Mobility and MANET Intelligent Transportation Systems
Rolland Vida

## Slide 2: Restricted directional flooding
Location-Aided Routing (LAR)
Use the position information of the destination node to limit the flooding
Introduces the notion of Expected Zone
  The zone where the destination is expected to be
  Estimation, based on the previous location of the destination, its speed and direction information
RREQ messages forwarded only inside a Request Zone
  The Request Zone includes the Expected Zone, together with the area linking the source with the Expected Zone

## Slide 3: LAR Expected Zone, Request Zone
X = the last known position of the destination D, at time t0
Y = the current position of the destination node D at time t1 (S is not aware of it)
r = (t1 - t0) * [estimated speed of D]
X
Y
r
Expected Zone
X
Y
r
S
Request Zone
B
A

## Slide 4: LAR Request Zone (2)
RREQ messages forwarded only inside the Request Zone
  The Request Zone might be the smallest rectangle including the source and the Expected Zone
  E.g., in the example, B forwards the RREQ, but A does not
The Request Zone explicitly defines whether the RREQ message should be dropped or not
Each node knows its own position, knows if it is inside the Request Zone or not

## Slide 5: LAR Request Zone (3)
If the source did not estimate well the position of the destination, the Request Zone might not contain it  the route discovery will fail!
After a timeout, the source starts a new search…
  Increases the size of the Request Zone;
  If needed, the entire network is included in the Request Zone
The following steps of LAR are similar to DSR
  In the RREQ message we include the path, step by step
  The destination sends back a RREP, following this path
  The path is then included in the header of the data packet
  Routes have to be refreshed from time to time

## Slide 6: LAR versions: Adaptive Request Zone
The Request Zone stored in the RREQ can be modified by each internal node, if
  It has fresher information about the destination
  AND the resulting Request Zone is included in the original one
S
B
Request zone created by B
Original Request zone determined by S

## Slide 7: LAR overview
Advantages
  The area of spreading of the RREQ message is limited
  Smaller overhead for route discovery
Drawbacks
  Nodes have to know their location

## Slide 8: Distance Routing Effect Algorithm for Mobility (DREAM)
Uses information about position and speed (as in LAR) for reducing the area flooded with data packets
Data is distributed by flooding, as opposed to LAR, where we only use flooding to discover the best route

## Slide 9: DREAM localization
1. Expected zone
(„as in LAR”)
3. Node A limites the flooding inside a cone where A is the apex
2. Data is flooded inside a cone where S is the apex, the expected zone is the base
S
D
A

## Slide 10: DREAM distance effect
Nodes periodically broadcast their position
„Distance effect” = Remote nodes move with a smaller angular speed.
 Close nodes should refresh their data more often
  Playing with the time-to-live (TTL) field
  Adaptive TTL

## Slide 11: CBF (Contention Based Forwarding)
In position-based routing solutions a node learns about the position of its neighbors via periodic beacon messages
  Mobility and energy-efficiency should be taken into account when calculating the frequency of beaconing
Proposal CBF (Contention Based Forwarding)
  Greedy forwarding, without any knowledge on the position of the neighbors
  Distributed next hop selection, hop-by-hop
  Advantages:
    Each node has to know only its own position
    No burden on the network because of the beacon (hello) messages
Comment: In some cases, if local maximum is reached, recovery mode might have to be activated, but this is a different problem.

## Slide 12: Contention Based Forwarding
How it works:
  The next hop is selected based on a contest
  Suppression: lowers the probability of collisions, as normally just one node is selected as next hop
Steps:
  The source broadcasts the message to its neighbors.
  Each node sets a timer for its own retransmission
    The timer inversely proportional to the distance form the source
  The timer of the furthest away node will expire first
  He retransmits, all the others hear it, and cancel their own retransmission
Decentralized selection of the next hop

## Slide 13: Vehicle-to-vehicle communication
„Traditional” ad hoc protocols:
  Proactive: DSDV (not detailed)
    High signalling to build and maintain routes that will constantly change in case of cars
  Reactive: AODV, DSR
    Slow topology discovery and route setup
    Not efficient for cars, as they move faster
  Position-based: LAR, DREAM
    Needs localization service
    In some cases it leads to local maximums, needs a recovery mode
    In urban scenarios there is a high chance for such local maximums, the physical distance is not so relevant when many buildings obstructing the communication
New solutions needed for vehicle-to-vehicle (V2V) communication

## Slide 14: AODV versions for VANETs
AOMDV: Multipath
  Not only one path is stored, but all those that were discovered
    This can be done without extra burden, as the path discovery is anyhow based on flooding
  If the primary path is broken, we can switch rapidly to a back-up path
    We need to search for new paths only if all the previously known paths are broken (or their number is getting very low)
SD-AOMDV: Speed and Direction
  The speed and direction of nodes is taken into account when selecting the best path out of the discovered ones
  A node can be next hop only if it goes in the same direction, with roughly the same speed
R-AOMDV: Retransmission count
  Takes into account the quality of the links, besides the hop count
    Link quality: number of retransmissions at MAC layer, until a successful retransmission
  Problem: link quality changes rapidly
  Cross-layer optimization – information from lower layers is used for routing at networking layer

## Slide 15: AODV versions for VANETs
AODV+PGB: Preferred Broadcast Group
  If the next hop is too close, the message does not advance rapidly
  If the next hop is too far, there is a high chance for the link to break
  Proposal: select as next hop nodes which are at a medium distance (the signal strength is average), they will form the Preferred Group
BAODV: Bus-AODV
P-AODV
I-AODV
Improved-AODV
AODV-BD
AODV-VANET
etc.

## Slide 16: Link-stability based routing
Movement Prediction based Routing (MOPR)
  Takes into account the position, speed and direction of the cars
  Builds routes with nodes that move in similar ways

## Slide 17: DTN: Delay Tolerant Network
If nodes are sparse, the network connectivity can be broken
Topology holes will appear
This can be handled by the carry-and-forward method
  Data-mules
It is possible if the message is still valid in spite of the delay
Mobility prediction is very useful

## Slide 18: VADD: Vehicle-Assisted Data Delivery in VANET
Carry-and-forward, optimized to the lowest delivery delay
  Prefers radio links, as they are faster than using data mule cars
  If data has to be carried by a car, it chooses the fastest car that goes in the good direction
  Dynamic routing step by step
  VADD delay model
    Distances between intersections
    Average vehicle density on each segment
    Average vehicle speed on each segment
  Stochastic model
    We cannot calculate in advance the entire path
    It depends on whether in a given intersection, at a given moment there will be a car to forward the message in a given direction, or not
    We can calculate probabilities

## Slide 19: GeOpps: Geographical Opportunistic Routing
Assumes that cars know in advance their trajectory
  Using some navigation, travel planner software
Next hop selected in three steps:
  Each neighbor calculates for its trajectory the closest point to the destination
  It calculates how much time it takes to that closest point
  If the trajectory of one of the neighbors gets closer to the destination than that of the current node, then the packet is taken over
If the car changes its trajectory, everything should be recalculated

## Slide 20: VANET broadcast protocols
We have a target zone, within which all the vehicles should receive the message (Broadcast Domain)
  However, the load on the network should be minimized, (avoid broadcast storms)
DECA: Density-Aware Reliable Broadcasting
  Does not use position information
  Beacon messages sent to discover neighbors
  Network load is minimized by chosing as next hop the neighbor that has most neighbors

## Slide 21: Intelligent flooding through gossiping
Messages are rebroadcast or dropped with a given probability p
  Carefully Localized Urban Dissemination (CLoUD)
The drop probability on a given road segment depends on the probability of cars on that segment heading towards the source of the flooding (where the danger was detected)
Needs a traffic database
  Turn probabilities at each intersection
  Stop probability on each segment
  Average traffic density in different periods of the day
Increasing reliability with a voting mechanism
  The message is dropped only if there are sufficent votes to drop it
Miklos Mate, Rolland Vida, „Reliable Gossiping in Urban Environments”, in Proceedings of 72nd IEEE Vehicular Technology Conference VTC-Fall, Ottawa, Canada, September 2010.

## Slide 22: Intelligent flooding through gossiping
Simulation results for the CLoUD protocol
  Digital map of Budapest, warmer colors mean more messages received by that car
  If the problem occurs on a main road (left), the message is spread more broadly
  If the problem occurs on a side road (right), the flooding dies out fast

## Slide 23: VANET Multicast protocols
There is a given area inside which all cars should receive the message (Zone of Relevance)
The multicast group is implicitely defined by the position of the cars
The source is not necessarily inside the ZOR, so first the packet should be delivered to the ZOR, through unicast routing, and then flood the ZOR
  E.g., information about traffic jam is not interesting for those already in the jam
  The alert should be sent to those who can still avoid it

## Slide 24: Mobicast
Mobile Just-in-time Multicasting
The Zone of Relevance, or Delivery Zone, moves with a given speed
  E.g., give way to the ambulance
We should ensure that within some space-time coordinates, each car that enters the Delivery Zone should receive the message before it enters the zone, or just on entering the zone

## Slide 25: Mobicast
Forwarding Zone
  Preceeds the Delivery Zone
  Nodes in this zone rebroadcast the message
Hold&Forward Zone
  They only store the message, and retransmit it only when entering the Forwarding Zone